## Slide 1: Large GEM Detectors for Tracking at Forward Rapidities
Marcus Hohlmann
Florida Institute of Technology
RHIC Spin Collaboration Meeting
Forward Spectrometer Hardware
BNL – March 9, 2017

## Slide 2: Outline
GEM principle
Large-area GEMs in experiments
  EIC detectors
  CMS forward muon upgrade
R&D on large-area GEMs for EIC
  Construction techniques
  Prototype designs and performances
Outlook

## Slide 3: GEM Principle
1cm
e-
Detector volume filled with
e.g. Ar/CO2 70:30 gas mixture
Ar+
CO2+
Micro-pattern gas detector (MPGD)
Anode strips
+
-
300 – 500 V (on each GEM)
Triple-GEM
detector
CMS GEM upgrade TDR

## Slide 4: Large-area GEM Uses
Examples in Nuclear and High Energy Physics:
ALICE
  TPC upgrade
CMS
  Forward muon upgrade
PRad
  XY tagger for calorimeter
Super Big Bite
  Main tracking
EIC detectors
  Forward tracking
GEMs are usually considered
“large” if they are > 1m long.
~

## Slide 5: Large GEMs for EIC Detectors
All proposed EIC detector concepts feature a form of large GEM tracker at forward and backward rapidities:
BeAST
ePHENIX
JLAB IP1
R&D effort dedicated to EIC forward tracking since 2011:
Florida Tech & U. Virginia (eRD6), Temple U. (eRD3)

## Slide 6: CMS Forward Muon Upgrade
Large GEMs were originally developed at CERN for the CMS forward muon upgrade project:
R&D program 2009-17 (with Fl. Tech participation)
  Mastering of single-mask etching of Cu-Kapton base material made GEMs larger than ~ 30 cm × 30 cm feasible
  Mechanical stretching and assembly of GEM foils makes internal spacers obsolete & allows re-opening of detector if needed (no gluing).
  Ten full-size GEM detectors installed in 2017 (slice test)
Technical Design Report for GEM upgrade in first muon station for High-Lumi. LHC approved 9/2015
Currently preparing mass production of 160 GEM detectors & second TDR for two other muon stations

## Slide 7: CMS GEM – Mechanical Construction
Purely mechanical assembly and GEM foil stretching:
CMS GEM TDR (CERN LHCC-2015-012)
3 large GEM foils
in a stack
Readout PCB
Drift PCB
(steel)
No spacers

## Slide 8: CMS GEM Upgrade
10o
superchambers
short
long
  “GE1/1” GEM subsystem in region 1.5 < |η| <2.2
  100 trapezoidal triple-GEM Superchambers (2 ch.)
  Long and short versions (1.5 or 1.6 < |η| <2.2)
  36 superchambers in each endcap
Muon
Endcap
Station 1
GE1/1
Front-end
Chamber
Installation planned for 2019
Muon
Endcap
Station 1

## Slide 9: CMS GEM Slice Test Installation
Commissioning
currently ongoing:
- Gas, HV on
- Electronics
powered
Muon
Endcap
Station 1
January 2017

## Slide 10: EIC GEM R&D: Construction
The three eRD3/6 FT groups are investigating different detector construction techniques:
Constructing detector purely mechanically & without any spacers as in CMS (Florida Tech)
Gluing stretched foils to FR4 spacer frames that are then mechanically assembled (U. Va.)
Gluing entire detector and inserting kapton rings between GEMs as spacers (Temple)

## Slide 11: Assembly with Bolted Spacer Frames (U. Va.)
Low material in active area
No honey comb support but keep spacers
Light material for GEM frames
High strength material for external support frames
Bolts & O-ring to seal the chambers
Chamber's characteristics
Example: Exploded 3D view of PRad GEM design
High strength material frame
Light material G10 as
GEM support frames
Bolts and O-ring to
seal the chamber
spacers
Courtesy Kondo Gnanvo, U.Va

## Slide 12: Assembly with Glued Frames (Temple)

## Slide 13: EIC GEM R&D: Readout
The three eRD3/6 FT groups are investigating also different signal readout techniques:
2D-readout with U-V strips (U. Va.)
2D-readout with R-φ readout strips (Temple)
1D-readout with radial zigzag strips that minimizes the number of strips and electronic channels to minimize cost while maintaining good spatial resolution (Florida Tech)

## Slide 14: First U-V Readout Prototype (U. Va.)
Courtesy Kondo Gnanvo, U. Va.

## Slide 15: R,φ-strip Readout Design (Temple)
2D strips in R and φ coordinates. Implemented as strip-pad design with vias.
Courtesy Matt Posik, Temple U.
Based on
STAR FGT

## Slide 16: First Zigzag-strip Readout (FIT)
CMS GEM detector equipped with a readout with radial zigzag strips on a PCB
Number of strips and readout channels are reduced by factor 3 relative to CMS readout
Zigzag strips cover radial range R ≈ 1.6 - 2.6 m in 8 eta sectors
Azimuthal strip angle pitch of 1.37 mrad; 128 strips per sector
Prototype tested in beam at Fermilab (2013)
Performance: Angular resolution of ~193 µrad (362 µm at R = 1.88 m)
Produced zigzag strip PCB
GEM assembly
(foils on drift PCB)
Radial zigzag strip
design
NIM A 811 (2016) 30
1 m

## Slide 17: EIC GEM R&D: Mult. Scattering
The three eRD3/6 FT groups are investigating methods to reduce overall detector material:
Remove or reduce Cu on GEM foils (U. Va.)
Replace solid drift and readout PCBs with carbon fiber composite frames (Florida Tech)
Reduces multiple scattering of tracks in the GEM detectors. Helps with:
matching electron tracks to EM cluster
seeding RICH ring reconstruction from incidence of hadron tracks on the RICH

## Slide 18: EIC GEM R&D: Next Prototypes
Adjust the GEM detector geometry to accommodate the geometry of an actual EIC forward tracker:
      R = 8 – 98 cm radial coverage
      Δφ = 30.1o azimuthal coverage
EIC R&D group designed a 1-m scale common GEM foil, which satisfies the requirements of all three assembly techniques to save cost
8 GEM foils were produced at CERN and delivered to Florida Tech and U. Va.

## Slide 19: Overall EIC FT Geometry
Design for an
EIC forward tracker disk composed of 12 such trapezoidal GEM detectors
Active areas of chambers overlap
due to 30.1o chamber design.

## Slide 20: Common EIC GEM Foil Design
Foil width (at the large R end) is limited to 560 mm due to material limit of 610 mm
25 mm margins needed for foil production
Trapezoid with a length of 903.57 mm, widths of 43 mm and 529 mm (active area).
Active area is divided into 8 HV sectors in R direction at inner R and 18 HV sectors in azimuthal directions at outer R. Reduces energy of any potential discharges.
Each HV sector is ~100 cm2 and gaps between sectors are 0.1 mm.
HV connections are made at wide end
560 mm (available design width)
610 mm (base material)
903.57 mm
30.1o
opening angle
HV sectorization
GEM foil produced at CERN

## Slide 21: Modified Mechanical Stretching (FlT)
Stack of 5 foils (3 GEM foils, 1 drift foil, and 1 readout foil)
No spacers
5-foil stack

## Slide 22: Carbon Fiber Frames (FIT)
5-foil stack
Carbon fiber frame
Mechanical support structures are outer frames with windows (e.g. aluminized mylar foil, not shown here) instead of solid PCBs to reduce radiation length in the active area
Frames are made from carbon fiber composites that have high strength to take up the tension from the stretched foils
Exploded assembly view
Assembled detector
Carbon fiber frames
5-foil stack
Gas seal frame

## Slide 23: CF Composite R&D (FIT)
Trimmed quarter-frame (test piece, 175 g)
Raw full drift frame before trimming
Carbon Fiber Composite:
Araldite epoxy (AY103)
Intermediate-modulus uni-directional
carbon fiber (“IM7”)
8 layers
Produced in-house

## Slide 24: Non-linearity of First Zigzag Readout
Scans across strips at 3 different radii
2D stage and highly collimated X-ray gun at BNL
“spine”
Reconstructed position vs. X-ray position (azimuthal)
Overetching of tips and underetching of valleys of zigzag strips creates “spines” along strip centers
GEM avalanche induces signal only on single strip
Without charge sharing among adjacent strips:
  Readout is insensitive to hit positions near the strip centers
  Overall spatial response is non-linear
  Spatial resolution degrades

## Slide 25: Improved Zigzag Strip Readout Design
The design pushes the PCB manufacturing limit since spaces are below 3 mils (76 um)
Produced a foil readout board at CERN to verify that there is no problem with producing high-quality zigzag strips on a large-area kapton foil at CERN
Same design is implemented on large 1-m zigzag readout foil being produced at CERN
Industrial
PCB
(10×10 cm2)
CERN
Foil
(10×10 cm2)
Zigzag strips interleave almost all the way to centers of both neighboring strips:
strip center
strip center

## Slide 26: Much Improved Linearity
Mean centroid measurement vs. X ray position (scan across strips)
Flat regions insensitive to hit positions.
Linear response over whole range
> 95% events fire 2 or 3 strips.
New board (same angle pitch)
old design
new design
Previous zigzag design

## Slide 27: Spatial Resolution
Spatial resolution (µrad / μm) | Vdrift (V) | Approx. gas gain | Strips with angle pitch 4.14 mrad, r ≈ 229 mm |  |  | Strips with angle pitch 1.37 mrad, r ≈ 784 mm |  | 
 |  |  | 2-strip clusters | 3-strip clusters | 2 & 3-strip clusters | 2-strip clusters | 3-strip clusters | 2 & 3-strip clusters
Industrial PCB | 3340 | 3000 | 288 / 66 | 480 / 110 | 384 / 88 | 57 / 45 | 97 / 76 | 84 / 66
CERN foil | 3340 | 3000 | 397 / 91 | 393 / 90 | 397 / 91 | - | - | -
CERN foil | 3380 | 4000 | - | - | - | 57 / 45 | 92 / 72 | 71 / 56
Previous PCB |  |  | - | - | - |  |  | 193 µrad
Measured resolutions for improved zigzag-strip readout boards:
Linear resolutions (well) below 100 µm

## Slide 28: EIC Zigzag Readout Foil (FIT)
Sector 1
Sector 2
Sector 3
4
5
Sec. Nr. | Strip type | No. of strips | Angle pitch (mrad) | Sector Length (cm)
1 | Straight | 128 | 4.14 | 12
2 | Zigzag | 128 | 4.14 | 12
3 | Zigzag | 384 (3×128) | 1.37 | 22
4 | Zigzag | 384 | 1.37 | 22
5 | Zigzag | 384 | 1.37 | 22
Adopt the improved zigzag strip design but use straight strips in small innermost sector 1
Divide readout into 5 main eta sections
Produce r/o on a foil material (<200 µm thickness) so that total material in detector is reduced
Total number of channels is 1152 (=128*9)
Only 9 APV chips to read out the full detector
Foil is a 2-layer design; signal routing from strips to connectors for APV front end was a challenge
Foil currently in production at CERN
Expect delivery by end of March 2017
Readout connectors (Panasonic 130-pin)
30.1o
opening angle

## Slide 29: Summary & Outlook
Large-area GEM detectors have become quite popular with a diverse set of experiments
Active EIC forward GEM tracking R&D since 2011
    Conceptual design for full EIC FT disk
    Built a common 30.1o GEM foil
    Developing & testing different assembly methods and readout designs
    Second round of full-size prototyping in progress
    Planning tests with X-rays and possibly beam in 2017
EIC Forward Tracking R&D readily applicable to RHIC detectors for forward spin physics

## Slide 30
Thank you!

## Slide 31: Backup

## Slide 32: GE1/1: Muon Measurement
GE1/1 creates a large lever arm with the CSC ME1/1 chambers
  Enables precise measurement of muon direction
  Much improved Level-1 trigger momentum resolution and lower rates in otherwise a problematic region of the detector
X3 reduction
Maintain low pT online threshold, keep < 5 kHz rate, high efficiency
Lever arm - trigger
32

## Slide 33: First Iteration
The U. Va group has assembled and tested a 1-m long triple-GEM detector equipped with 2D stereo angle (U-V) strips.
Assembly method: glue foils to frames that are held together to with screws.
Resolutions of 60 urad in azimuthal direction and better than 550 um in radial direction are achieved.
Ref.: NIM A 808 (2016) 83

## Slide 34: GEM foil scanning (Temple)
Scanned 40 cm × 40 cm GEM foils from commercial supplier and small CERN foils with an automated CCD camera setup. Currently upgrading CCD scanner so that large GEM foils can also be scanned.
NIM A 617 (2010) 196-198
NIM A 802 (2015) 10-15
Example: Inner hole diameter distributions

## Slide 35: STAR FGT Quarter Section
HV layer
GEM layers (1-3)
2D readout board
Readout module
APV chip
HV board
Interconnect board
Terminator board
Pressure volume
Pressure volume
Pressure volume

## Slide 36: Readout design at FIT group zigzag strips
-> Type A has been tested in our previous prototype (arXiv:1508.07046), type B will be chosen for the next prototype. The reason is: type B design gives better charge sharing and shows less non-linear response.
Simple model simulation results (courtesy of Alexander Kiselev, BNL)

## Slide 37: Readout design at FIT group zigzag strips
Type A
Type B
Strip center
Neighbor strip centers
Angle pitch: α
Reference lines
F*α, 0<F<1
Start R
R step
-> Four parameters to construct a zigzag strip: α, F, startR, stepR.
-> Two types of zigzag structure can be made: (1) type A, a zigzag strip not exceeding the two reference lines; (2) type B, a zigzag strip covers centers of the two neighbor strips.
Figure by A. Ataei

## Slide 38
X (arbitrary unit)
Y (arbitrary unit)
Centers of strips
Reference lines

## Slide 39
X (arbitrary unit)
Y (arbitrary unit)

## Slide 40: Electronics – SRS and APVs
Ref.: 2013 JINST 8 C03015

## Slide 41: Signal routing from readout strips to connectors
0.5 mm
Connectors for APV chips
Signal lines are blue (top side)
Zigzag strips are red (bottom side)
Connection made with vias

## Slide 42
Optimization of the zigzag strip readout design – X ray scan results
Resolution studies with CERN board for strips with angle pitch 1.37 mrad, radius ≈ 784 mm
Cluster strip multiplicity = 2
Cluster Strip multiplicity = 3
Centroid
Residuals
Residual dist.
FIT

## Slide 43
Optimization of the zigzag strip readout design – Results of X-ray scans at BNL
Mean centroid vs. X-ray position
Best board from PCB comp.
CERN
kapton foil
board
Strip angle pitch 4.14 mrad, radius in EIC ≈ 229 mm
Strip angle pitch 1.37 mrad, radius in EIC ≈ 784 mm
-> The response is much more linear than with the original zigzag design!
-> There are a few flat regions due to backlash of the motor when data taking was interrupted.
FIT

## Slide 44: Readout design at U. Va group 2D stereo angel strips (U-V strips)
Angles between U-V strip is 12 deg.
20 APVs (2560 channels) to read out a detector.
K. Gnanvo, U.Va

## Slide 45: 2D (U-V strips) readout with zebra connection concept
Zebra contacts
Zebra holder on the adapter
Zebra’s side (to R/O U-V strip)
Panasonic side (to FE card)
Top strip
Bottom strip
Kapton
Test on a small 10x10 triple GEM prototype
Contact of U and V strips on either side of the R/O foil
Small GEM prototype with zebra
2D U-V strips readout board
Zebra to Panasonic adapter PCB

## Slide 46: Preliminary results on small 2D (U-V strips) triple GEM prototype with Zebra connection
X-ray
bad zebra contact
COMPASS readout
standard connection
U-V strips readout
zebra connection
Distribution of pedestal rms (noises) over 512 APV25 chs
Pedestal noise level comparable to standard COMPASS 2D readout
No effect of the zebra connection on noise level
Occupancy for U and V strips: Linear dependence with strip length is shown
Cluster size > 3.5 ⇨ improvement in spatial resolution
Uniformity of the gain uniformity: (accumulated ADC / numbers of hits)