A Guide to Garfield

By: Jeremy Janney

Advisor: Dr. Marcus Hohlmann

April 20, 2004

A Guide to Garfield

Table of Contents

- Garfield	1

- &CELL	2

- &FIELD	5

- &MAGNETIC	6

- &GAS	7

- &Drift	10

File Output and Examples

GARFIELD

Garfield’s purpose is to model and simulate two and three dimensional drift chambers.  Garfield uses field maps for these drift chambers as the basis for its calculations.  Particle drift including, diffusion, avalanches, and induction can be treated in the three-dimensional case.

Garfield begins in the &MAIN section and has seven subsections, &CELL, &MAGNETIC, &GAS, &OPTIMISE, &FIELD, &DRIFT, and &SIGNAL.  I will deal with the cell, magnetic, and gas definition and the visualization sections.  They will contain all of the commands that I found useful during my research.

Garfield allows you to abbreviate most commands, to a certain extent.  For instance, &MAGNETIC can be entered as &MAG or the PLANE command can be entered as PL.

Garfield can be treated like a programming language, so batch files can be used or you can copy code directly into Garfield.

If you see an ‘ (apostrophe) in the online help guide and the code does not seem to work, that is not an ‘ (apostrophe).  It is actually a backward apostrophe and is entered by holding SHIFT and hitting the ~ (tilde) key.

&CELL

You can enter this section by typing &CELL.  Entering this section clears any cell information currently in memory.  Cell structures can be saved and recalled in this section.

Commands:

| Options | Options for layout plotting |
| --- | --- |
| Plane | Enters a plane |
| Rows | Wire list header |
| Tube | Defines a tube surrounding the wire(s) |
| Write | Writes a compact format dataset |
| Get | Opens a compact cell description |

GET

Retrieves a compact cell description written by WRITE.  Any cell information in memory will be cleared.

Format:

GET file

get [`cell1.dat`]

PLANE

Defines an infinite equipotential plane at constant x, y, phi or a circular plane with constant radius, r.  Wires cannot be placed at the center of planes.  This geometry is taken care of by the TUBE command.  Planes cannot be used with a TUBE geometry.

Format:

PLANE direction V-potential

PLANE x=4, V=1000

pl phi=20

OPTIONS

Selects options for the cell.  Layout plots the cell when the &CELL section is left.  Wire-markers plots wires as markers instead of circles with the size of the wire.

Format:

Options [NOLAYOUT | LAYOUT] [NOWIRE-MARKERS | WIRE-MARKERS]

OPT layout

OPT wire-markers

ROWS

Rows is used to enter wires.  (I only have used sense wires.)  The following properties can be entered for the wire with this command:

- Label that identifies the kind of wire (S for sense)

- the wires position, potential and diameter

The default diameter is 0.01 cm.

Format:

ROWS

Label n diameter x y V

……

ROWS

s * * 0 0 2000

(places a sense wire at the origin with a V of 2000)

TUBE

A tube is a pipe that surrounds a wire.  The tube can be round, triangular, or hexagonal.  The TUBE command is useful because a wire cannot be placed at the exact center of a cell defined by circular plane.

Format:

TUBE [Radius r] [Voltage V]

tube r=4, v=3000

tube hexagonal r=3

WRITE

This command writes the current cell data to a file that can be retrieved with the GET command.

Format:

WRITE DATASET file [member] [remark]

wr data cell1.dat cell1 rem “a cell”

wr cell2.dat cell2 “another cell”

&FIELD

The field section is used for visual inspection of electrostatic elements within the chamber.  The main command of this section is PLOT-FIELD.

| AREA | Sets the plotting area size |
| --- | --- |
| PLOT-FIELD | Field plotting instruction |

AREA

Sets the limits for the box at which you want to look, particles are not allowed to drift outside the box.  Area commands are found in the field and drift sections.

Format:

AREA [xmin ymin xmas ymax]

Area -4 -4 4 4

Area -.01 -.01 .01 .01

PLOT-FIELD

Plots the electrostatic and magnetic field in quite a few ways.  You can combine several plots to save CPU time.

Format:

PLOT-FIELD	[CONTOUR] [GRAPH] [HISTOGRAM] [SURFACE] [VECTOR]

Plot hist vector surf cont

(The above plots the histogram, the vectors, surface and the contour plot.)

You can plot for E, V, B, and the differentials of these elements by adding them at the end of the graph call.

Plot vector EX, EY, EZ

&MAGNETIC

You can enter this section by typing &MAGNETIC or &MAG.  Any information pertaining to the B-field can be entered through this section.

| COMPONENTS | Enters the B-field components |
| --- | --- |

COMPONENTS

This command sets the components of the magnetic field.  If in spherical coordinates, the radial and angular components must be zero.

Format:

COMPONENTS X Y Z

comp 0 0 25 T

comp 0 0 1 G

&GAS

You can enter this section by inputting &GAS.  In this section, you will input the gas mixture to be used when drifting electrons and ions.  The Magboltz plug-in will calculate the drift velocity, diffusion, Townsend and attachment coefficients.  The Heed plug-in takes care of clustering.

| MAGBOLTZ | Magboltz gas mixture (accurate) |
| --- | --- |
| MIX | Schultz-Gresser gas mixing (approximate) |
| PRESSURE | Sets pressure |
| TEMPERATURE | Sets temperature |
| WRITE | Stores the gas description |
| OPTIONS | Plotting of gas tables |
| GET | Retrieves the stored gas description |

MAGBOLTZ

Calls the Magboltz plug-in to compute drift velocity, longitudinal and transverse diffusion coefficients, and Townsend and attachment coefficients for electrons.  Magboltz takes cross-sections of non-elastic processes into account, this makes Magboltz more accurate than the Mix command.  If using a Magnetic field, make sure to input it before calling Magboltz as it takes the B-field into account.

Magboltz sets the Temp and Pressure at 300 K and 760 Torr.

Format:

MAGBOLTZ [gas mixture in %]

Magboltz argon 70 co2 30

Magboltz cf4 100

MIX

Computes the drift velocity and diffusion for a mix of gasses.  This method neglects ionization effects and therefore lacks accuracy.

Format:

MIX [gas mixture in %]

Mix argon 70 co2 30

mix co2 100

PRESSURE

Sets the pressure of the gas.

Format:

PRESSURE pressure [unit]

Pressure 760 torr

Pressure 1 bar

TEMPERATURE

Sets the temperature of the gas.

Format:

TEMPERATURE temperature [unit]

Temperature 300 K

Temperature 4 C

WRITE

Writes a compact format of the gas data that can be retrieved by the GET command.  This is recommended when using Magboltz or Mix because they are so CPU intensive.  Writing takes place upon the close of the GAS section.

Format:

WRITE DATASET file [member] [remark]

Write {gas_file, gas_member}

Write {`ar70co230.gas`}

OPTIONS

Selects gas related options, namely plotting drift velocity.

Format:

OPTIONS [NOGAS-PLOT | GAS-PLOT]

Options gas-plot

GET

Retrieves a compact gas description written by WRITE.  Any gas information in memory will be cleared.

Format:

GET file

get [`ar70co230.gas`]

&DRIFT

This section deals with displaying the movement of electrons and ions in the chamber.  Both the gas and cell sections are important to this section.

| AREA | Sets the size of the drift area window |
| --- | --- |
| DRIFT | Plots the drift lines and isochrones |
| LINES | Sets lines default |
| PLOT-FIELD | Plots drift-related values |
| TRACK | Sets the particle trajectory |

AREA

Sets the limits for the box at which you want to look, particles are not allowed to drift outside the box.  Area commands are found in the field and drift sections.

Format:

AREA [xmin ymin xmas ymax]

Area -4 -4 4 4

DRIFT

Plots ion and electron drift lines along with isochrones.  There are 5 starting points: the EDGES of the AREA, the TRACK, the surface of SOLIDS, the surface of WIRES, and the ZEROES of the electrostatic field.  The only options I have dealt with are the EDGES, the TRACK, and the surface of WIRES.

Format:

DRIFT {	EDGES [LEFT |NOTLEFT] [RIGHT | NOTRIGHT]…

[UP | NOT UP] [DOWN | NOTDOWN] [LINES lines]

TRACK [NOVELOCITYGRAPH | VELOCITY GRAPH]

WIRES [LINES lines]

[NOISOCHRONES | ISOCHRONES delta_t]

[LINE-PLOT | NOLINE-PLOT] [ELECTRON | ION]}

drift edges lines=20 isochrones .01

drift edges lines=20 wires lines=20

(Once again, you can enter multiple graphs to save valuable CPU time.)

LINES

Sets the default number of lines.

Format:

LINES lines

LINES 20

PLOT-FIELD

In the drift section, you can plot the same graphs as the FIELD section, but for the drift velocity, diffusion, and avalanche if such data is available.

Format:

PLOT-FIELD	[ CONTOUR] [GRAPH] [HISTOGRAM] [SURFACE] [VECTOR]

PLOT HIST DIFFUSION VECTOR VDX, VDY SURF CONT

TRACK

Defines the track that is used with the DRIFT TRACK command.  I have not yet gotten DRIFT TRACK to work correctly.

Format:

TRACK [x0 y0 z0 | xf yf zf]

Examples of Output

To create a basic tubular potential graph like this, this is the code:

&cell

opt wire-markers

tube r=2

rows

s * * 0 0 2000

&field

plot surf

Adding E or Ex, Ey, will change the output of the graph from potential to e-field.  You can also map drift velocity.  The following example is a bit more complicated, but it shows the drift velocity plot.

Magboltz:

Running Magboltz takes quite some time depending upon your computer setup, so I suggest saving the gas file whenever you are finished running Magboltz.  The code to save a Magboltz file is as follows:

&GAS

Global gas_file=`co2100.gas`

Opt gas-plot

Write {gas_file}

Temp 300 K

Pressure 1 atm

Magboltz co2 100

The first line defines the variable gas_file as the file output name.  The second line tells Garfield that you want a plot of drift vs. e-field after you leave the Gas section.  The Write command will write the Magboltz results to the file `co2100.gas` when you leave the Gas section.  Next, define the temperature and pressure, and then finally run Magboltz.

Remember, you can retrieve the gas file in the Gas section with the following code:

&GAS

Get {`co2100.gas1}

The code for this parallel line system plot is:

&cell

opt wire-markers

pl x=-4 v=0

pl y=-4 v=0

pl x=4 v=0

pl y=4 v=0

rows

s * * 2 2 2000

s * * -2 -2 2000

&gas

get {`ar70co230.gas`}	(Opens a gas file that I already ran through Magboltz)

&drift

plot vector

The code for this parallel line system plot is:

&cell

opt wire-markers

pl x=-4 v=0

pl y=-4 v=0

pl x=4 v=0

pl y=4 v=0

rows

s * * 2 2 2000

s * * -2 -2 2000

&gas

get {`ar70co230.gas`}

&drift

area -3.9 -3.9 3.9 3.9	(Reset the area to exclude the planes)

drift edges lines=20 noisochrones	(drifts from the edges of the chamber)