Brookhaven National Laboratory

Appointment Report

June 1, 2004 – July 30, 2004

Guest Name: Georgia Karagiorgi

Guest Number: U9710

Supervisor: Dr. Craig Woody,

PHENIX, BNL

Purpose of Appointment:

The purpose of the appointment was to provide undergraduate research experience in the field of experimental nuclear and high energy physics in a professional research environment.

Description of Work:

The scope of the work was the development and support of various detectors that are going to be a part of the PHENIX experiment at the RHIC (Relativistic Heavy Ion Collider) facility at Brookhaven National Laboratory. It involved the testing and optimization of parts and setups employed in various detectors, such as the Hadron Blind Detector (HBD) and the Time Projection Chamber (TPC).

Training:

Upon arrival at the Lab, the following safety training courses were required to be completed:

- Site Orientation for Guests

- Cyber Security Training

- Radiation, ALARA, and Hazards for Physics Dept.

- Collider User Training

- PHENIX Awareness Training

- Radiation Worker I

- Electrical Safety I

- Compressed Gas Safety

Projects and Methods:

- Testing and comparison of GEM foils from different manufacturers

The upgrading of existing detectors as well as the installation of new detectors that employ Gas Electron Multipliers (GEM’s), required the testing of performance of GEM foils produced by different manufacturing companies, in order to determine which GEM foils show the most ideal and reliable behavior.

Sets of GEM foils from three different manufacturers, the Instrumentation Division at CERN, Tech Etch, and 3M, were tested for their impedance, leakage current, gain stability in time, gain with respect to foil potential, and % resolution.

Each set was tested in a triple-GEM detector setup (see figure 1), in an Ar/CO2 (70/30) gas environment. The gas within the detector volume was constantly being recycled through a gas input and output, at a relatively low flow rate. The drift, transfer, and induction gap electric fields were kept constant for all measurements, as shown below:

Edrift = 0.4kV/cm

Etransfer1 = 2.5kV/cm

Etransfer2 = 3kV/cm

Einduction = 3.5kV/cm

Figure 1: Triple-GEM Setup

The detector was illuminated with a semi-collimated X-ray beam from a 5.9keV 55Fe source. The X-rays ionized the gas within the drift volume of the detector, and produced clusters of primary charge, which cascaded through the transfer and induction gaps, and were collected at the anode, as a signal. The signal was then read into a single ADC channel, and a pulse high distribution was obtained. From the pulse height distribution, the gain was determined.

The stability measurement was conducted at a potential of 340V applied across each GEM foil; each potential (including the drift, transfer, and induction potentials) was provided by a separate HV supply. The stability measurement extended over an average period of 24hrs for each set of foils. A separate measurement for 370V across each GEM foil was performed for the CERN foils, to verify their stability at a higher gain.

The gain measurement was conducted for the range of 320V –380V across each GEM foil; again, each potential was provided by a separate HV supply.

# Transmittance measurements of UV light in Ar gas

A transmittance monitor is in the process of being developed and optimized to be used as a part of the HBD, a detector which is planned to be installed in PHENIX by the end of year 2005. The HBD requires a pure CF4 gas environment, which is transparent to UV light, in order to work efficiently. A transmittance monitor is currently being developed in order to monitor the UV transmittance within the gas volume of the HBD and ensure that O2 and H2O concentrations within the gas volume, which are the main contributors to UV absorbance, remain well below tolerable levels during the HBD operation.

Using a McPherson 234 Vacuum UV Spectrometer, UV light transmittance measurements were conducted in Ar, a gas which is also transparent to UV light. (Bottled (4.8) Ar gas was used for all the measurements.) The spectrometer part of the monitor (see figure 2) is always under vacuum, and it contains a 100W deuterium lamp of output wavelength range 1100-2000Å. A high vacuum system is provided for the both the spectrometer and the detector part. The detector part is also supplied with a gas input and output, and it contains two photomultipliers: one in regular PMT mode, and the second one in photodiode (PD) mode, which acts as a monitoring device for the first one. Two gas analyzers, one for O2 and one for H2O, are connected to the gas system after the gas output of the detector and record the real-time concentration of O2 and H2O in a ppm scale.

Figure 2: UV Transmittance Monitor Setup

For each transmittance measurement, two consecutive scans – one in Ar gas and the following one in vacuum – were taken. The transmittance was obtained by taking the ratio of the output current of the PMT in Ar gas over its output current in vacuum at each photon wavelength. By varying the O2 and H2O concentration levels in the gas volume, a family of transmittance curves was obtained for UV photons of wavelength 1100-2000Å. For each measurement the O2 and H2O ppm levels were recorded.

During gas scans, the Ar gas was constantly being recycled at a flow rate ranging from 100-1000sccm. A micrometer valve was installed in the gas input, which regulated the flow (and concentration) of bottled O2 gas introduced into the gas volume.

# Measurements of drift velocity of charge clusters in a TPC setup

The TPC detector is a future detector project that is planned to be a part of the PHENIX experiment. It will be used for multiple purposes, one of which is particle identification. A TPC test setup has been built and is currently being tested for measurements of charge cluster drift velocity, charge cluster longitudinal and lateral spread, and spatial resolution of signal.

The setup consists of a series of circular electrodes stacked up over a triple-GEM setup of CERN foils (see figure 3). The total potential applied between the topmost electrode and the anode reaches up to 35kV. The electrodes and GEM setup are all in the same gas environment. The gas which is currently being used for the drift velocity measurement is Ar/CO2 (70/30). Two X-ray sources, a permanent one on top of the electrodes, and retractable one on top of the GEM setup are used to generate charge clusters at different regions of the detector.

Figure 3: TPC Test Setup

Before any drift velocity measurements were taken, the quality of the gas mixing system that was used to supply the TPC setup with gas had to be tested. The lower X-ray source was used with the GEM setup inside the TPC, and a series of gain curves was obtained both in pre-mixed, bottled Ar/CO2 (70/30), and in Ar/CO2 (70/30) mixed using the system in the lab. The GEM configuration and parameters were the same as the ones used in the setup for testing GEM foils from different manufacturers (Section I).

A Class IV Continuum Minilite Laser is used for measuring the drift velocity of charge clusters in different gases. The laser fires at a rate of 10-15Hz in the horizontal direction between the two top-most electrodes. The beam is focused in the center of the electrode stack, ionizing a number of gas molecules at the focal point, thus generating a charge cluster. The charge cluster propagates downwards towards the GEM setup due to the uniform electric field that exists in the center of the electrode stack, and a signal is eventually collected and read out using a Tektronix TDS 7254B oscilloscope.

The oscilloscope also reads a second signal, generated by a photodiode aligned with and triggered by the laser beam. The time difference between the peaks of the two signals is measured, and, given the drift distance (32cm), the drift velocity can be calculated with respect to different electric field configurations.

Work Results:

    - Testing and comparison of GEM foils from different manufacturers

All foils showed similar behavior regarding impedance and leakage current. For all foils tested (CERN, TECH ETCH, and 3M) the impedance was found to be ~100Gohm, and the leakage current was found to be ~sub-nA. In addition, during six days of continuous operation at deltaV(foil) = 340V, none of the sets of foils tripped.

The % resolution, however, varied with different sets of foils. For the TECH ETCH foils, the % resolution in Ar/CO2 (70/30) for deltaV(foil)=340V was ~(25±2)%, for the CERN foils it was ~(21±2)%, and for the 3M foils it was ~(29±2)%.

Also, the TECH ETCH foils showed some charging effects, as shown in plot 1.

Plot 1:  Observation of Charging Effects in TECH ETCH Triple GEM

in Ar/CO2 (70/30)

Plot 2: Gain Stability Measurements in Ar/CO2 (70/30)

Plot 3:  Gain Measurements in Ar/CO2 (70/30)

# Transmittance measurements of UV light in Ar gas

Plot 4: Latest UV Transmittance Measurement in Ar Gas with respect to different O2 and H2O levels in the Gas Volume

(using Regulated O2 Flow through Micrometer Valve)

The transmittance measurements are currently in progress, and more transmittance curves are to be taken with respect to higher levels of O2 and H2O.

# Measurements of drift velocity of charge clusters in a TPC setup

The first stage of drift velocity measurements, which was the testing of the accuracy of the lab’s gas mixing system has been complete. Plot 5 shows the results after comparison of gain curves in both pre-mixed, bottled gas, and gas mixed using the lab’s gas mixing setup. All gain curves are further compared to the gain curve of the CERN foils obtained during the testing of GEM foils from different manufacturers. The gain curves showed a maximum variation of ~50% at higher deltaV(foil) applied. However, overall, the two gas systems seemed to be consistent.

Drift velocity measurements are currently in progress in Ar/CO2 (70/30) for electric fields inside the detector volume ranging from 0.1kV/cm to 1.2kV/cm.

Plot 5: Comparison of Gain of TPC GEM Setup in different Ar/CO2 (70/30)

Gas Systems

Conclusions:

The different measurements performed showed good and promising results; however, more work is still needed to be done, especially on the development and optimization of the UV transmittance monitor, and the TPC test setup.

The purpose of the appointment was fulfilled, since the interaction with various detector projects introduced aspects of a relatively wide spectrum of the work processes and methods involved in experimental nuclear and high energy physics.